## Slide 1: Embedding-Based Placement of Processing element Networks on FPGAs for Physical Model Simulation
Bailey Miller*, Frank Vahid*, Tony Givargis**
*Univ. of California, Riverside
**Univ. of California, Irvine
Supported by the NSF (CNS1016792, CPS1136146), and Semiconductor Research Corporation (GRC 2143.001)
Intern at SpaceX

## Slide 3: Models of physical world that run in real-time
http://www.nhlbi.nih.gov/
Test cyber-physical systems
Physical mockup
Transducer
models
Environment
model
Digital mockup

## Slide 4: Issue: Real-time achieved via inaccuracy
Weibel lung complexity
4 gen: 32 ODEs
6 gen: 128 ODEs
8 gen: 512 ODEs
10 gen: 2048 ODEs
“2-3 minutes to simulate one breath accurately”
V[1],R[1]
V[2],R[2]
V[7],R[7]

## Slide 5: Earlier results
Frank Vahid, UCR 5
0
100
200
300
400
500
600
700
800
900
1000
Weibel
Neuron
Weibel + gas
Hemodynamic
Weibel + hemo
Performance (ms)
PC(1)
PC(4)
GPU
HLS / FPGAs
Speedup vs real-time
PC(1): 0.8x
PC(4): 3.1x
GPU: 1.6x
HLS/FPGA: 3.2x
1430
1490
1522
1184
Parallel computations +
Neighbor communication
 Seem like great match for FPGAs

## Slide 6: Network of synchronized PEs on FPGAs
FPGA
Digital mockup
General Processing Element
Iterative ODE solver (Euler/RK4)
0.1 ms / 0.01 ms timestep
PE
PE
PE
1 PE: 300 MHz

## Slide 7: Earlier results
0
100
200
300
400
500
600
700
800
900
1000
Weibel
Neuron
Weibel + gas
Hemodynamic
weibel + hemo
Performance (ms)
PC(1)
PC(4)
GPU
HLS
General PEs
Speedup vs real-time
PC(1): 0.8x
PC(4): 3.1x
GPU: 1.6x
HLS: 3.2x
General PE: 4.9x
1430
1490
1522
1184

## Slide 8: Current work Problem: More PEs  Lower frequency
FPGA
Inter-PE critical path
FPGA
DSP
INST
MEM
DATA
MEM
Internal PE critical path
11-gen Weibel model, Virtex6 240T FPGA, general PEs
Real ODEs/sec
Lost ODEs/sec due to freq drop
Notes: The bottom-left figure shows how place and route does increasingly more poor at meeting timing constraints for larger PE networks.
The bottom-right figure shows:
BLUE: The actual ODEs/sec throughput for the implementations of the design points in the bottom left figure.
RED: The ODEs/sec throughput that was lost because place/route introduced critical paths into the design.
BLUE+RED: The total theoretical ODEs/sec throughput that would be possible if the frequency wasn’t impacted by place/route (Assuming 1 PE on Xilinx Virtex6 can run no faster than 300MHz)

## Slide 9: Earlier approach
10K iterations
150K iterations
Convert virtual PEs to physical circuits using FPGA place-route
1
2
Phase
Maps ODEs to virtual PEs using simulated annealing

## Slide 10: This work: Main idea
FPGA
Graph embedding: Map guest graph to host graph, minim. max wire length
Guest
Host
Virtual PEs
Physical PEs
Use physical model structure to avoid using FPGA placement (Phase 2)

## Slide 11: Phase 2 – Map virtual PEs to physical PEs
Frank Vahid, UCR 11
FPGA
1
2
3
…
FPGA
FPGA
Embedding algorithm
H-tree embedding
Linear embedding
Direct map embedding
Guest
Host
[1] Zienicke, P. 1990. Embeddings of Treelike Graphs into 2-Dimensional Meshes. (WG '90).
[2] Aleliunas, R., and Rosenberg, A.L. 1982. On Embedding Rectangular Grids in Square Grids. (Computers ‘82).
[3] Berman, F., and Snyder, L. 1987. On mapping parallel algorithms into parallel architectures, (PDC, ‘87).

## Slide 12: 2D grid of physical PEs
EqP1
EqV1
EqP2
EqV2
EqP3 EqV3
EqP4
EqV4
EqP7
EqV7
EqP5
EqV5
EqP6
EqV6
FPGA
Bypass FPGA placement
EqP1
EqV1
EqP4
EqV4
EqP2
EqV2
EqP5
EqV5
EqP2
EqV2
EqP6
EqV6
EqP7
EqV7
(Phase 1: May require "graph folding" first to reduce #PEs)

## Slide 13: Compare/backup: Simulated annealing
FPGA
Cost function:
C = w1*sum + w2*max + w3*gaps
Sum = sum of wire distances
Max = max wire length (Euclidean dist.)
Gaps = wires across architectural features
FPGA
P1
P1
P2
Neighbor function:
Swap PEs based on distance to neighbors
Notes: This slide details the custom cost and neighbor functions for the SA approach.
The top right correlation plot just shows that higher cost = lower frequency.
The bottom right graph shows that our custom neighbor is better than random swapping.
The neighbor function algorithm goes like this:
1. Select a random pe (P1)
2. Average the edges connected to P1 to find an area in the grid that places P1 as close as possible to P1’s neighbors (Circled Region)
3. Average the edges of all pes in Circled Region. Select the pe (P2) from Circled Region that has neighbors closest to P1.
4. Swap P1 with P2

## Slide 14: Results
No placement strategy
Simulated annealing placement
Embedding placement
4 generations shown
5 generations shown
5 generations shown
Notes: Xilinx tools must trade off between area/power. With no extra placement constraints, place/route creates a more dense design optimized for power. With placement constraints, place/route can’t optimize for power as well, since we have forced the tool to spread the design out and use more space in the chip (same # of LUTS, just spread out more).

## Slide 15: Results
Not routable
Strategy | # LUTS | # BRAM | #DSP | Equivalent LUTs
None | 58362 | 512 | 256 | 306682
SA | 58567 | 512 | 256 | 306887
Embed | 58569 | 512 | 256 | 306889
No impact on size
2D Neuron model - 256PE – Xilinx Virtex6
Strategy | Total power (mW) | Dynamic power (mW) | Static power (mW)
None | 15525 | 8744 | 6481
SA | 16604 | 10013 | 6590
Embed | 19859 | 12999 | 6859
20% more power
Using Xilinx XPower Analyzer

## Slide 16: Results/Conclusions
http://www.meti.com/
Speedup vs real-time (avg)
PC(1): 0.8x
PC(4): 3.1x
GPU: 1.6x
HLS: 3.2x
General PE: 4.9x
Grph emb(GPE): 11.2x
Custom PE: 6.1x
Heterog PE: 34.5x
(Grph emb(HPE): 48.5x)
Graph emb. gives additional speedup
  FPGAs: Fastest cost-effective execution of physical models
  http://www.youtube.com/watch?v=ThUKVhqoA3Q
Future
  Manycore device
  Beyond testing CPS
    Implement end-products
Speedup / dollar
Heterog PE
3.0x better than PC(4)
4.5x better than GPU
CPU (I7-950 + Intel X58 board): $480
GPU(GTX460 + I3-540 + H55 board): $380
FPGA (Xilinx Virtex6 240T-2 board): $1800

## Slide 17: Questions?
Frank Vahid, UCR 17